## Slide 1: A Lumped-Parameter Modeling, Calibration, and Capacity-Measure Framework for Flux Generation in Symmetric Multipole Electromagnetic Actuators

## Slide 2: Current-based lumped-parameter modeling and calibration
E. Validation
Interpolation Point Algorithm for workspace pseudocode
Algorithm 1 Generate Interpolation Points
Input: Na, R
Output: pa (Ntot × 3) // interpolation point
1: d ← R / Na // point to point distance
2: Ntot ← 1 + 6·Na // total number of points
3: pa ← zeros(Ntot, 3)
4: E ← eye(3) // unit vectors of three axes
5: cnt ← 1; pa(cnt, :) ← [0, 0, 0] // center point
6: for j = 1 to 3 do
7: for s ∈ {+1, −1} do // ± direction
8: for i= 1 to Na do
9: cnt ← cnt + 1
10: pa(cnt, :) ← s · i · d · E(j, :) // i-th point on axis j
11: end for
12: end for
13: end for
14: return pa
Algorithm 2 Barycentric Interpolation
Input: pa (Ntot × 3), p (Np × 3) // FEM points , b(p) (Np × 3 × Ns) // FEM Flux density
Output: b(pa) (Ntot × 3 × Ns)
1: T ← DelaunayTriangulation(p) // rebuild connectivity
2: for q = 1 to Ntot do
3: (tetID, λ) ← PointLocation(T, pa(q, :)) // enclosing tetrahedron
// λ=(​, ​, ​, ​): weight
4: (v1, v2, v3, v4) ← ConnectivityList(T, tetID) // 4 interpolation nodes
    // (v1, v2, v3, v4) : FEM node number
5: for s = 1 to Ns do
6: b(pa)(q, :, s) ← Σ λi · b(p) (vi, :, s), i = 1,…,4 // weighting
7: end for
8: end for
9: return b(pa)

## Slide 3: Current-based lumped-parameter modeling and calibration
E. Validation
This figure illustrates the magnetic flux path when pole P2 is excited. The left figure presents a top view, with the theoretical magnetic charge locations labeled to clarify the magnetic charge concept used in this study. The right figure shows a three-dimensional view of the same model, in which the theoretical magnetic charge locations and the magnetic flux distribution can be clearly observed.
The threshold used in the 3D plot on the right is 0.1 mT, meaning that only values greater than 0.1 mT are displayed in the figure.

## Slide 4: Current-based lumped-parameter modeling and calibration
E. Validation
Workspace radius
Percentage count
Modeling error

## Slide 5: Quantitative Assessment of Multi-Pole Actuators
DesignA
DesignB
P1
P2
P3
P6
P4
P5
P1
P2
P3
P4
P6
P5
Setup: The assessment that follows compares two six-pole actuator designs, Design 1 on a circular yoke and Design 2 on a planar square frame. Both are described by the same lumped-parameter model and use the pole numbering P1-P6 shown here.
Sharing the model form and the pole numbering, the two differ only in geometry, so their calibrated parameters can be compared directly in the following slides.

## Slide 6: Quantitative Assessment of Multi-Pole Actuators
DesignA
Mean | 14.6246
 | 14.6246
d
Percentage count
Mean | 0.8836
 | 0.8836
Isotropy
Percentage count
Histogram resolution 0.02
Histogram resolution 0.01

## Slide 7: Quantitative Assessment of Multi-Pole Actuators
DesignB
Mean | 39.4683
 | 39.4683
Mean | 0.5415
 | 0.5415
Histogram resolution 0.02
Histogram resolution 0.01
Capacity measure
Percentage count
Isotropy
Percentage count

## Slide 8: Quantitative Assessment of Multi-Pole Actuators
DesignB(Have gap)
Mean | 23.9991
 | 23.9991
Mean | 0.4820
 | 0.4820
Histogram resolution 0.02
Histogram resolution 0.01
Capacity measure
Percentage count
Isotropy
Percentage count

## Slide 9: Reference
, where