## Slide 1: A Lumped-Parameter Modeling, Calibration, and Capacity-Measure Framework for Flux Generation in Symmetric Multipole Electromagnetic Actuators

## Slide 2: Current-based lumped-parameter modeling and calibration
E. Validation
Localization: Determine which tetrahedron contains each query point and return its coordinates relative to the four vertices.
Barycentric Interpolation:
  Let the coordinates of the four vertices be:
  Let the coordinates of the interpolation point be:
  Where (The volume of the sub-tetrahedron formed by replacing vertex with )
Repeat Steps 4 and 5 until all interpolation points have been processed.
Interpolation Point Algorithm for sensor area
Input ， These represent the numbers of divisions required along the three actuation axes
Divided along its three actuation axes according to the following .
  with an additional center point
  Therefore, the total number of points is
Load the FEM data and filter out the air nodes.

## Slide 3: Current-based lumped-parameter modeling and calibration
E. Validation
The convergence criterion is defined as follows: check whether and remain within ±0.2% of their steady-state values for ten consecutive points. If this condition is satisfied, the first point is taken as the convergence point.
Long
 | Number of points at convergence | Calibration value at the convergence point | Calibration value using all nodes | Steady-state value
Single parameter | points |  | 874.25 | 871.00
 |  |  | 9.67 | 9.69
Eighteen parameters | points |  | 873.96 | 868.57
 |  |  | 10.75 | 10.64
 | Number of points at convergence | Calibration value at the convergence point | Calibration value using all nodes | Steady-state value
Single parameter |  |  |  | 
Eighteen parameters |  |  |  | 

## Slide 4: Current-based lumped-parameter modeling and calibration
E. Validation
The convergence criterion is defined as follows: check whether and remain within ±0.2% of their steady-state values for ten consecutive points. If this condition is satisfied, the first point is taken as the convergence point.
Zhi peng
 | Number of points at convergence | Calibration value at the convergence point | Calibration value using all nodes | Steady-state value
Single parameter | points |  | 7 | 7
 |  |  | 3 | 3
Eighteen parameters | points |  | 6 | 5
 |  |  | 3 | 3
 | Number of points at convergence | Calibration value at the convergence point | Calibration value using all nodes | Steady-state value
Single parameter |  |  |  | 
Eighteen parameters |  |  |  | 

## Slide 5: Current-based lumped-parameter modeling and calibration
E. Validation
Calibration results
Single parameter(25 points)
Eighteen parameters(13 points)
Calibration results obtained using the interpolation points determined above.
Long calibrate results

## Slide 6: Current-based lumped-parameter modeling and calibration
E. Validation
Calibration results
Single parameter(7 points)
Eighteen parameters(7 points)
Calibration results obtained using the interpolation points determined above.
Zhi peng calibrate results

## Slide 7: Current-based lumped-parameter modeling and calibration
E. Validation
Calibration results
Long bias at measure coordinate system
Zhi peng bias at measure coordinate system
Transforming into the measurement coordinate system makes the primary direction of the magnetic charge displacement more apparent. It can be observed that the displacement of P1 occurs mainly in the plane, which is physically reasonable.

## Slide 8: Current-based lumped-parameter modeling and calibration
E. Validation
This figure shows the trends of the calibration results for and for Long-Fei and Zhi-Peng, using the minimum number of points required for each working range.
If no convergence point can be found within a given range for either the single-parameter model or the eighteen-parameter model, all nodes within that range are used for calibration instead. This is used only to illustrate the trend, and the values within that range are not used as a basis for calibration.
Long
Zhi peng

## Slide 9: Current-based lumped-parameter modeling and calibration
E. Validation
Long
Zhi peng

## Slide 10: Current-based lumped-parameter modeling and calibration
E. Validation
Setup: The calibration side is identical to the previous slide: the same R sweep, the same converged reduced design at each R. What changes is the evaluation: the predict is computed on every real FEM node inside R.
Long
Zhi peng

## Slide 11: Current-based lumped-parameter modeling and calibration
E. Validation
This figure shows the fitting results for the FEM nodes within R≤150μm after both models were calibrated over the same region using their respective convergence points.This figure overlays the distributions of the two models. The red distribution is noticeably more concentrated than the blue one, indicating that the eighteen-parameter model performs better than the one-parameter model in fitting the magnetic field.
Workspace radius:
 | Single | Eighteen
Mean | 0.2878mT | 0.0340mT
Long(:1771)
Zhi peng (:1791)
Resolution:2.8uT
Resolution:17uT
 | Single | Eighteen
Mean | 3.0658mT | 0.2190mT

## Slide 12: Current-based lumped-parameter modeling and calibration
E. Validation
Setup: Calibration is performed using the eighteen-parameter calibration points, followed by fitting to the FEM nodes within the workspace.
 |  | Peak value |  | Mean error | 
Left figure | 1771 | 7.237% | 10.2452mT | 0.0340mT | 
Right figure | 14082 | 0.3491% | 10.4684mT | 0.1271mT ( | 0.3019mT (
 |  |  |  | Mean error | 
Left figure | 1771 | 7.237% | 10.2452mT | 0.0340mT | 
Right figure | 14082 | 0.3491% | 10.4684mT |  | 
Long
Resolution:2.8uT

## Slide 13: Current-based lumped-parameter modeling and calibration
E. Validation
Setup: Calibration is performed using the eighteen-parameter calibration points, followed by fitting to the FEM nodes within the workspace.
 |  | Peak value |  | Mean error | 
Left figure | 1791 | 6.4954% | 29.1094mT | 0.2190mT | 
Right figure | 14066 | 0.4751% | 30.7330mT | 0.4294mT ( | 1.2666mT (
 |  |  |  | Mean error | 
Left figure | 1791 | 6.4954% | 29.1094mT | 0.2190mT | 
Right figure | 14066 | 0.4751% | 30.7330mT |  | 
Zhi peng
Resolution:17uT

## Slide 14: Current-based lumped-parameter modeling and calibration
E. Validation
These two figures show the differences in the calibrated magnetic charge locations between the two models. The upper row presents the magnetic charge locations calibrated by the one-parameter model, shown using side views of poles P1 and P2. It can be clearly seen that, for the lower pole, some of the magnetic charge locations are located outside the pole. This is because the one-parameter model constrains the magnetic charges to lie along the actuator coordinate axes. The lower row presents the results of the eighteen-parameter model, in which the magnetic charge locations of the lower pole move inside the pole. This is more consistent with the expected physical situation. Moreover, the error histograms shown above also indicate that these magnetic charge locations are more consistent with the theoretical positions.
Long

## Slide 15: Current-based lumped-parameter modeling and calibration
E. Validation
These two figures show the differences in the calibrated magnetic charge locations between the two models. The upper row presents the magnetic charge locations calibrated by the one-parameter model, shown using side views of poles P1 and P2. It can be clearly seen that, for the lower pole, some of the magnetic charge locations are located outside the pole. This is because the one-parameter model constrains the magnetic charges to lie along the actuator coordinate axes. The lower row presents the results of the eighteen-parameter model, in which the magnetic charge locations of the lower pole move inside the pole. This is more consistent with the expected physical situation. Moreover, the error histograms shown above also indicate that these magnetic charge locations are more consistent with the theoretical positions.
Zhi peng

## Slide 16: Hall-sensor-voltage-based lumped-parameter modeling and calibration
This figure conveys the sensing concept: the Hall sensor measures the pole's leakage flux. The colour-coded arrows show the flux channelled inside the cone toward the tip, while the dashed arrows around the pole are the part that escapes through the lateral surface and returns through the air. The sensor (green patch) is mounted on that surface, so it sits in the leakage field rather than in the field between the tips, and the red arrow n⁺ marks the positive sense of what it reads (b·n⁺).

## Slide 17: Hall-sensor-voltage-based lumped-parameter modeling and calibration
Single parameter
Eighteen parameters
Long

## Slide 18: Hall-sensor-voltage-based lumped-parameter modeling and calibration
Single parameter
Eighteen parameters
Moving the sensors further out along the pole flank leaves the field model completely untouched: the effective length, the charge-offset matrix and the fit error are identical to the closer mounting — and identical to the current-based results as well, since both reduce to the same transfer matrix. Only the voltage scale changes: further from the tip the leakage field is weaker, so the measured voltages drop and the voltage gain rises to compensate. This is structural rather than coincidental — the field model is fitted from the workspace field alone, and the sensor geometry enters only afterwards, when the excitation is re-expressed in volts. The predictive accuracy of the model is therefore independent of where the sensor is mounted, and the mounting position becomes a free design choice, bounded in practice only by keeping the sensor voltage within its linear range.
Long

## Slide 19: Hall-sensor-voltage-based lumped-parameter modeling and calibration
Single parameter
Eighteen parameters
Moving the sensors further out along the pole flank leaves the field model completely untouched: the effective length, the charge-offset matrix and the fit error are identical to the closer mounting — and identical to the current-based results as well, since both reduce to the same transfer matrix. Only the voltage scale changes: further from the tip the leakage field is weaker, so the measured voltages drop and the voltage gain rises to compensate. This is structural rather than coincidental — the field model is fitted from the workspace field alone, and the sensor geometry enters only afterwards, when the excitation is re-expressed in volts. The predictive accuracy of the model is therefore independent of where the sensor is mounted, and the mounting position becomes a free design choice, bounded in practice only by keeping the sensor voltage within its linear range.
Zhi peng

## Slide 20: Hall-sensor-voltage-based lumped-parameter modeling and calibration
Single parameter
Eighteen parameters
Moving the sensors further out along the pole flank leaves the field model completely untouched: the effective length, the charge-offset matrix and the fit error are identical to the closer mounting — and identical to the current-based results as well, since both reduce to the same transfer matrix. Only the voltage scale changes: further from the tip the leakage field is weaker, so the measured voltages drop and the voltage gain rises to compensate. This is structural rather than coincidental — the field model is fitted from the workspace field alone, and the sensor geometry enters only afterwards, when the excitation is re-expressed in volts. The predictive accuracy of the model is therefore independent of where the sensor is mounted, and the mounting position becomes a free design choice, bounded in practice only by keeping the sensor voltage within its linear range.
Zhi peng

## Slide 21: Quantitative Assessment of Multi-Pole Actuators
DesignA
DesignB
P1
P2
P3
P6
P4
P5
P1
P2
P3
P4
P6
P5
Setup: The assessment that follows compares two six-pole actuator designs, Design 1 on a circular yoke and Design 2 on a planar square frame. Both are described by the same lumped-parameter model and use the pole numbering P1-P6 shown here.
Sharing the model form and the pole numbering, the two differ only in geometry, so their calibrated parameters can be compared directly in the following slides.

## Slide 22: Quantitative Assessment of Multi-Pole Actuators
DesignA
P1
P2
P3
P2
P4
P5
P6
P1
P4
P5
P6
P3
The three reference planes are mutually orthogonal and all pass through the origin; the inset shows how they sit inside the pole-tip sphere, each disc extending out to that sphere. On every plane the calibrated model is evaluated point by point and the capacity measure is mapped in polar form, with the two pole pairs lying in that plane marked on the rim. The pattern is the same everywhere: the capacity is lowest at the center, grows steadily outwards, and reaches its maxima in four lobes pointing at the in-plane poles, with troughs between them. This is the gain signature of Design A: the gain is not uniform over the workspace but is smallest at the center and largest along the pole axes near the tips, and its variation with direction follows the pole layout directly. Because the three maps are indistinguishable, the gain field carries the full symmetry of the six-pole arrangement — six poles of equal strength, arranged as three opposing pairs whose axes are mutually perpendicular. The consequence is that the gain is limited not by any particular plane or direction, but by radial position: the lowest gain of the whole workspace sits at its center.

## Slide 23: Quantitative Assessment of Multi-Pole Actuators
DesignA
Same three planes and the same calibrated model as before, but now mapping the isotropy. The picture is the exact complement of the capacity map: isotropy is highest at the centre and decays outwards in an almost circular pattern, reaching its lowest values at the rim. The reason is geometric — at the centre all six poles are equidistant, so the three singular values are nearly equal and the system can push with almost the same strength in any direction; moving outwards means approaching one pole pair while receding from the other two, so one singular value grows while the others shrink and the ratio collapses. Again the three planes are indistinguishable, confirming that the isotropy inherits the symmetry of the pole layout.
P1
P3
P2
P4
P2
P5
P6
P1
P4
P5
P6
P3

## Slide 24: Quantitative Assessment of Multi-Pole Actuators
DesignA
The three distributions separate clearly, and the separation is asymmetric: the largest singular value is roughly twice the other two and spreads over a wide range with a long tail towards high values, while the second and third are narrow and overlap heavily. Over most of its workspace Design A therefore has one dominant direction and two comparable, weaker ones, rather than three directions of similar strength; the isotropy deficit seen on the previous slide is driven mainly by the strong axis pulling away, not by the weakest axis collapsing. The long tail belongs to the points closest to the pole tips — the same points that form the four red lobes of the capacity map on slide 14.
Both histograms have the same resolution (22.17uT/A).
Mean | 15.722 | 14.403 | 13.852
 | 15.722 | 14.403 | 13.852

## Slide 25: Quantitative Assessment of Multi-Pole Actuators
DesignB
Zhi-Peng delivers 2.71× the actuation strength of Long Fei (39.58 vs 14.62 mT/A). Both share the same pattern: weakest at the centre, strengthening toward the pole tips, and almost constant with direction within the calibration radius，the planar hexapole wins outright on strength, and it is a pure gain improvement — the field shape is not degraded, and the advantage holds uniformly across the workspace.
P4
P5
P6
P3
P3
P2
P4
P5
P6
P1
P2
P1

## Slide 26: Quantitative Assessment of Multi-Pole Actuators
DesignB
Zhi-Peng reaches only 0.62× the isotropy of Long Fei (0.544 vs 0.884). Long Fei's high-κ region is concentric about the origin, whereas Zhi-Peng's is offset, split into two diagonal lobes, and decays faster with radius. the gain is bought at the cost of isotropy. More importantly, Zhi-Peng's best-isotropy point is not the origin — Long Fei gives the most balanced three-axis control simply by staying at the centre, whereas Zhi-Peng offers no such sweet spot.
P3
P2
P4
P5
P6
P1
P2
P1
P4
P5
P6
P3

## Slide 27: Quantitative Assessment of Multi-Pole Actuators
DesignB
Mean | 50.196 | 45.304 | 27.105
 | 50.196 | 45.304 | 27.105
Both histograms have the same resolution (184.5uT/A).
The three singular values are σ₁ = 50.25, σ₂ = 45.39 and σ₃ = 27.26 mT/A. σ₁ and σ₂ differ by only 10.7 %, whereas σ₃ falls 40 % below σ₂ (σ₁/σ₃ = 1.84). All three distributions are tight，the controllable set is an oblate ellipsoid — two strong axes and one weak — not a sphere. The weakest third axis is the bottleneck of the whole actuator, since it sets the force available in the worst direction.

## Slide 28: Quantitative Assessment of Multi-Pole Actuators
DesignB(Have gap)
Zhi-Peng delivers 2.71× the actuation strength of Long Fei (39.58 vs 14.62 mT/A). Both share the same pattern: weakest at the centre, strengthening toward the pole tips, and almost constant with direction within the calibration radius，the planar hexapole wins outright on strength, and it is a pure gain improvement — the field shape is not degraded, and the advantage holds uniformly across the workspace.
P4
P5
P6
P3
P3
P2
P4
P5
P6
P1
P2
P1

## Slide 29: Quantitative Assessment of Multi-Pole Actuators
Zhi-Peng reaches only 0.62× the isotropy of Long Fei (0.544 vs 0.884). Long Fei's high-κ region is concentric about the origin, whereas Zhi-Peng's is offset, split into two diagonal lobes, and decays faster with radius. the gain is bought at the cost of isotropy. More importantly, Zhi-Peng's best-isotropy point is not the origin — Long Fei gives the most balanced three-axis control simply by staying at the centre, whereas Zhi-Peng offers no such sweet spot.
P2
P4
P5
P6
P1
P2
P1
P3
P4
P5
P6
P3
DesignB(Have gap)

## Slide 30: Quantitative Assessment of Multi-Pole Actuators
Mean | 32.34 | 27.588 | 15.54
 | 32.34 | 27.588 | 15.54
Both histograms have the same resolution (130.89uT/A).
The three singular values are σ₁ = 50.25, σ₂ = 45.39 and σ₃ = 27.26 mT/A. σ₁ and σ₂ differ by only 10.7 %, whereas σ₃ falls 40 % below σ₂ (σ₁/σ₃ = 1.84). All three distributions are tight，the controllable set is an oblate ellipsoid — two strong axes and one weak — not a sphere. The weakest third axis is the bottleneck of the whole actuator, since it sets the force available in the worst direction.
DesignB(Have gap)

## Slide 31: Quantitative Assessment of Multi-Pole Actuators
Mean | 24 | 39.468
 | 24 | 39.468
Histograms have the same resolution (0.05mT/A).
The three singular values are σ₁ = 50.25, σ₂ = 45.39 and σ₃ = 27.26 mT/A. σ₁ and σ₂ differ by only 10.7 %, whereas σ₃ falls 40 % below σ₂ (σ₁/σ₃ = 1.84). All three distributions are tight，the controllable set is an oblate ellipsoid — two strong axes and one weak — not a sphere. The weakest third axis is the bottleneck of the whole actuator, since it sets the force available in the worst direction.
DesignB(Have gap & No gap )
Mean | 0.4820 | 0.5415
 | 0.4820 | 0.5415
Histograms have the same resolution (0.011).

## Slide 32: Reference
, where

## Slide 33: Reference
P1
P2
P3
P6
P4
P5
DesignB
DesignC
P1
P5
P3
P2
P6
P4

## Slide 34: Reference
(7 points)

## Slide 35: Reference
Calibration results
 | esignB | DesignC
Mean | 0.5415 | 0.5023
 |  | DesignC
 | 0.5415 | 0.5023

## Slide 36: Reference
(1771 points)

## Slide 37: Reference
(1791 points)

## Slide 38: Reference
(13 points)

## Slide 39: Reference