## Slide 1: A Lumped-Parameter Modeling, Calibration, and Capacity-Measure Framework for Flux Generation in Symmetric Multipole Electromagnetic Actuators

## Slide 2: Current-based lumped-parameter modeling and calibration
E. Validation
Interpolation Point Algorithm for workspace pseudocode
Algorithm 1 Generate Interpolation Points
Input: Na, R
Output: pa (Ntot × 3)
1: d ← R / Na // division spacing
2: Ntot ← 1 + 6·Na // total number of points
3: pa ← zeros(Ntot, 3)
4: E ← eye(3) // unit vectors of three axes
5: cnt ← 1; pa(cnt, :) ← [0, 0, 0] // center point
6: for j = 1 to 3 do
7: for s ∈ {+1, −1} do // ± direction
8: for i = 1 to Na do
9: cnt ← cnt + 1
10: pa(cnt, :) ← s · i · d · E(j, :) // i-th point on axis j
11: end for
12: end for
13: end for
14: return pa
Algorithm 2 Barycentric Interpolation
Input: pa (Ntot × 3), p (Np × 3), b(p) (Np × 3 × Ns)
Output: b(pa) (Ntot × 3 × Ns)
1: T ← DelaunayTriangulation(p) // rebuild connectivity
2: for q = 1 to Ntot do
3: (tetID, λ) ← PointLocation(T, pa(q, :)) // enclosing tetrahedron
4: (v1, v2, v3, v4) ← ConnectivityList(T, tetID) // 4 interpolation nodes
5: for s = 1 to Ns do
6: b(pa)(q, :, s) ← Σ λi · b(p) (vi, :, s), i = 1,…,4 // weighting
7: end for
8: end for
9: return b(pa)

## Slide 3: Current-based lumped-parameter modeling and calibration
E. Validation
This figure illustrates the magnetic flux path when pole P2 is excited. The left figure presents a top view, with the theoretical magnetic charge locations labeled to clarify the magnetic charge concept used in this study. The right figure shows a three-dimensional view of the same model, in which the theoretical magnetic charge locations and the magnetic flux distribution can be clearly observed.
The threshold used in the 3D plot on the right is 0.1 mT, meaning that only values greater than 0.1 mT are displayed in the figure.

## Slide 4: Current-based lumped-parameter modeling and calibration
E. Validation
The convergence criterion is defined as follows: check whether and remain within ±0.2% of their steady-state values for ten consecutive points. If this condition is satisfied, the first point is taken as the convergence point.
Long
 | Number of points at convergence | Calibration value at the convergence point | Calibration value using all nodes | Steady-state value
Single parameter | points |  | 874.25 | 871.00
 |  |  | 9.67 | 9.69
Eighteen parameters | points |  | 873.96 | 868.57
 |  |  | 10.75 | 10.64
 | Number of points at convergence | Calibration value at the convergence point | Calibration value using all nodes | Steady-state value
Single parameter |  |  |  | 
Eighteen parameters |  |  |  | 
Number of point
Number of point
Number of point
Number of point

## Slide 5: Current-based lumped-parameter modeling and calibration
E. Validation
The convergence criterion is defined as follows: check whether and remain within ±0.2% of their steady-state values for ten consecutive points. If this condition is satisfied, the first point is taken as the convergence point.
Zhi peng
 | Number of points at convergence | Calibration value at the convergence point | Calibration value using all nodes | Steady-state value
Single parameter | points |  | 7 | 7
 |  |  | 3 | 3
Eighteen parameters | points |  | 6 | 5
 |  |  | 3 | 3
 | Number of points at convergence | Calibration value at the convergence point | Calibration value using all nodes | Steady-state value
Single parameter |  |  |  | 
Eighteen parameters |  |  |  | 
Number of point
Number of point
Number of point
Number of point

## Slide 6: Current-based lumped-parameter modeling and calibration
E. Validation
Calibration results
Single parameter(25 points)
Eighteen parameters(13 points)
Calibration results obtained using the interpolation points determined above.
Long calibrate results

## Slide 7: Current-based lumped-parameter modeling and calibration
E. Validation
Calibration results
Single parameter(7 points)
Eighteen parameters(7 points)
Calibration results obtained using the interpolation points determined above.
Zhi peng calibrate results

## Slide 8: Current-based lumped-parameter modeling and calibration
E. Validation
Calibration results
Long bias at measure coordinate system
Zhi peng bias at measure coordinate system
Transforming into the measurement coordinate system makes the primary direction of the magnetic charge displacement more apparent. It can be observed that the displacement of P1 occurs mainly in the plane, which is physically reasonable.

## Slide 9: Current-based lumped-parameter modeling and calibration
E. Validation
This figure shows the trends of the calibration results for and for Long-Fei and Zhi-Peng, using the minimum number of points required for each working range.
If no convergence point can be found within a given range for either the single-parameter model or the eighteen-parameter model, all nodes within that range are used for calibration instead. This is used only to illustrate the trend, and the values within that range are not used as a basis for calibration.
Long
Workspace radius
Workspace radius

## Slide 10: Current-based lumped-parameter modeling and calibration
E. Validation
This figure shows the trends of the calibration results for and for Long-Fei and Zhi-Peng, using the minimum number of points required for each working range.
If no convergence point can be found within a given range for either the single-parameter model or the eighteen-parameter model, all nodes within that range are used for calibration instead. This is used only to illustrate the trend, and the values within that range are not used as a basis for calibration.
Zhi peng
Workspace radius
Workspace radius

## Slide 11: Current-based lumped-parameter modeling and calibration
E. Validation
Long
Zhi peng
Both panels fit the point-charge model within R ≤ 150 µm. Sampling is the actuator-axis shell ladder — six pole axes Nr shells plus the centre , so Number of points = 6Nr+1, spanning 7 to 49. Frobenius error (%) is the relative error of against the full-grid fit, shown for the single- and eighteen-parameter models.
At their convergence points the reduced designs already reproduce the all-node closely: Long gives 2.66 % with the single parameter (25 points) and 1.71 % with eighteen (13 points); Zhi-Peng converges at 7 points for both, at 2.10 % and 0.39 %. The eighteen-parameter fit is consistently closer to the all-node solution (≈1.8× for Long, ≈5× for Zhi-Peng), with the planar design benefiting far more. Extending to 49 points improves every curve by under one percentage point, so the obtained at the convergence point already represents what the design can achieve and can replace the all-node calibration.
Number of point
Frobenius error
Number of point
Frobenius error
Number of point
Frobenius error
Number of point
Frobenius error

## Slide 12: Current-based lumped-parameter modeling and calibration
E. Validation
Setup: The calibration side is identical to the previous slide: the same R sweep, the same converged reduced design at each R. What changes is the evaluation: the predict is computed on every real FEM node inside R.
Predict error rises monotonically with workspace radius for both designs and degrades sharply beyond the 150 µm calibration radius: Long grows from 0.20 mT at R = 160 µm to 0.92 mT at 400 µm and 4.12 mT at 500 µm, while Zhi-Peng grows from 2.11 mT to 10.39 mT and 18.91 mT. The eighteen-parameter fit is lower at every radius, but its advantage collapses with R — from 7.6× to 1.07× for Long and from 13.2× to 1.8× for Zhi-Peng — showing that charge offsets correct near-field structure only and cannot compensate the far-field model error. Long remains about an order of magnitude more accurate than Zhi-Peng, so the conical hexapole extrapolates markedly better; for both, the model is trustworthy only near the calibration radius.
Long
Zhi peng
Workspace radius
Modeling error
Workspace radius
Modeling error

## Slide 13: Current-based lumped-parameter modeling and calibration
E. Validation
This figure shows the fitting results for the FEM nodes within R≤150μm after both models were calibrated over the same region using their respective convergence points.This figure overlays the distributions of the two models. The red distribution is noticeably more concentrated than the blue one, indicating that the eighteen-parameter model performs better than the one-parameter model in fitting the magnetic field.
Workspace radius:
 | Single | Eighteen
Mean | 0.2878mT | 0.0340mT
Long(:1771)
Zhi peng (:1791)
Resolution:2.8uT
Resolution:17uT
 | Single | Eighteen
Mean | 3.0658mT | 0.2190mT
Modeling error
Percentage count
Modeling error
Percentage count

## Slide 14: Current-based lumped-parameter modeling and calibration
E. Validation
Setup: Calibration is performed using the eighteen-parameter calibration points, followed by fitting to the FEM nodes within the workspace.
 |  | Peak value |  | Mean error | 
Left figure | 1771 | 7.237% | 10.2452mT | 0.0340mT | 
Right figure | 14082 | 0.3491% | 10.4684mT | 0.1271mT ( | 0.3019mT (
 |  |  |  | Mean error | 
Left figure | 1771 | 7.237% | 10.2452mT | 0.0340mT | 
Right figure | 14082 | 0.3491% | 10.4684mT |  | 
Long
Resolution:2.8uT
Modeling error
Percentage count
Modeling error
Percentage count

## Slide 15: Current-based lumped-parameter modeling and calibration
E. Validation
Setup: Calibration is performed using the eighteen-parameter calibration points, followed by fitting to the FEM nodes within the workspace.
 |  | Peak value |  | Mean error | 
Left figure | 1791 | 6.4954% | 29.1094mT | 0.2190mT | 
Right figure | 14066 | 0.4751% | 30.7330mT | 0.4294mT ( | 1.2666mT (
 |  |  |  | Mean error | 
Left figure | 1791 | 6.4954% | 29.1094mT | 0.2190mT | 
Right figure | 14066 | 0.4751% | 30.7330mT |  | 
Zhi peng
Resolution:17uT
Modeling error
Percentage count
Modeling error
Percentage count

## Slide 16: Current-based lumped-parameter modeling and calibration
E. Validation
These two figures show the differences in the calibrated magnetic charge locations between the two models. The upper row presents the magnetic charge locations calibrated by the one-parameter model, shown using side views of poles P1 and P2. It can be clearly seen that, for the lower pole, some of the magnetic charge locations are located outside the pole. This is because the one-parameter model constrains the magnetic charges to lie along the actuator coordinate axes. The lower row presents the results of the eighteen-parameter model, in which the magnetic charge locations of the lower pole move inside the pole. This is more consistent with the expected physical situation. Moreover, the error histograms shown above also indicate that these magnetic charge locations are more consistent with the theoretical positions.
Long

## Slide 17: Current-based lumped-parameter modeling and calibration
E. Validation
These two figures show the differences in the calibrated magnetic charge locations between the two models. The upper row presents the magnetic charge locations calibrated by the one-parameter model, shown using side views of poles P1 and P2. It can be clearly seen that, for the lower pole, some of the magnetic charge locations are located outside the pole. This is because the one-parameter model constrains the magnetic charges to lie along the actuator coordinate axes. The lower row presents the results of the eighteen-parameter model, in which the magnetic charge locations of the lower pole move inside the pole. This is more consistent with the expected physical situation. Moreover, the error histograms shown above also indicate that these magnetic charge locations are more consistent with the theoretical positions.
Zhi peng

## Slide 18: Hall-sensor-voltage-based lumped-parameter modeling and calibration
This figure conveys the sensing concept: the Hall sensor measures the pole's leakage flux. The colour-coded arrows show the flux channelled inside the cone toward the tip, while the dashed arrows around the pole are the part that escapes through the lateral surface and returns through the air. The sensor (green patch) is mounted on that surface, so it sits in the leakage field rather than in the field between the tips, and the red arrow n⁺ marks the positive sense of what it reads (b·n⁺).

## Slide 19: Hall-sensor-voltage-based lumped-parameter modeling and calibration
Single parameter
Eighteen parameters
Long

## Slide 20: Hall-sensor-voltage-based lumped-parameter modeling and calibration
Single parameter
Eighteen parameters
Moving the sensors further out along the pole flank leaves the field model completely untouched: the effective length, the charge-offset matrix and the fit error are identical to the closer mounting — and identical to the current-based results as well, since both reduce to the same transfer matrix. Only the voltage scale changes: further from the tip the leakage field is weaker, so the measured voltages drop and the voltage gain rises to compensate. This is structural rather than coincidental — the field model is fitted from the workspace field alone, and the sensor geometry enters only afterwards, when the excitation is re-expressed in volts. The predictive accuracy of the model is therefore independent of where the sensor is mounted, and the mounting position becomes a free design choice, bounded in practice only by keeping the sensor voltage within its linear range.
Long

## Slide 21: Hall-sensor-voltage-based lumped-parameter modeling and calibration
Single parameter
Eighteen parameters
Moving the sensors further out along the pole flank leaves the field model completely untouched: the effective length, the charge-offset matrix and the fit error are identical to the closer mounting — and identical to the current-based results as well, since both reduce to the same transfer matrix. Only the voltage scale changes: further from the tip the leakage field is weaker, so the measured voltages drop and the voltage gain rises to compensate. This is structural rather than coincidental — the field model is fitted from the workspace field alone, and the sensor geometry enters only afterwards, when the excitation is re-expressed in volts. The predictive accuracy of the model is therefore independent of where the sensor is mounted, and the mounting position becomes a free design choice, bounded in practice only by keeping the sensor voltage within its linear range.
Zhi peng

## Slide 22: Hall-sensor-voltage-based lumped-parameter modeling and calibration
Single parameter
Eighteen parameters
Moving the sensors further out along the pole flank leaves the field model completely untouched: the effective length, the charge-offset matrix and the fit error are identical to the closer mounting — and identical to the current-based results as well, since both reduce to the same transfer matrix. Only the voltage scale changes: further from the tip the leakage field is weaker, so the measured voltages drop and the voltage gain rises to compensate. This is structural rather than coincidental — the field model is fitted from the workspace field alone, and the sensor geometry enters only afterwards, when the excitation is re-expressed in volts. The predictive accuracy of the model is therefore independent of where the sensor is mounted, and the mounting position becomes a free design choice, bounded in practice only by keeping the sensor voltage within its linear range.
Zhi peng

## Slide 23: Quantitative Assessment of Multi-Pole Actuators
DesignA
DesignB
P1
P2
P3
P6
P4
P5
P1
P2
P3
P4
P6
P5
Setup: The assessment that follows compares two six-pole actuator designs, Design 1 on a circular yoke and Design 2 on a planar square frame. Both are described by the same lumped-parameter model and use the pole numbering P1-P6 shown here.
Sharing the model form and the pole numbering, the two differ only in geometry, so their calibrated parameters can be compared directly in the following slides.

## Slide 24: Quantitative Assessment of Multi-Pole Actuators
DesignA
Capacity measure
P1
P2
P3
P2
P4
P5
P6
P1
Capacity measure
P4
P5
P6
P3
The capacity measure 𝒞 for Design A is mapped on three mutually orthogonal actuator planes through the origin (–, –, –). The model is calibrated on the converged design within R ≤ 150 µm, then evaluated point by point out to the pole-tip sphere at R = 500 µm; the two pole pairs lying in each plane are marked on the rim.
𝒞 peaks on the rim along the pole directions (16.7–17.3 mT/A) and bottoms out on the rim between poles (13.2–13.3), while the centre sits at 14.39 mT/A and is identical on all three planes. Along a pole axis 𝒞 therefore rises monotonically with radius, but between poles it rises then falls, so the weakest actuation in the workspace lies on the rim between poles rather than at the centre — the centre is the most uniform point, not the weakest. The four lobes are not equal in strength: the lower poles P1/P3/P6 reach ≈16.69 and the upper poles P2/P4/P5 ≈17.32, a 3.8 % difference, and the arrangement of strong lobes differs on – from the other two planes — a direct signature of the upper/lower asymmetry of Long's half-cut geometry.

## Slide 25: Quantitative Assessment of Multi-Pole Actuators
DesignA
Same three actuator planes and the same calibrated model as the previous slide, now mapping isotropy = σ₃/σ₁ (dimensionless, colour scale 0–1). It is again evaluated point by point out to the pole-tip sphere at R = 500 µm, with the in-plane pole pairs marked on the rim.
is close to 1 at the centre and decays outwards, staying above 0.8 roughly within the calibration radius of 150 µm before degrading quickly. The decay is not circularly symmetric: at the rim, isotropy is worst along the pole directions and best between poles, differing by about a factor of two. Isotropy is therefore the exact complement of capacity — the rim along a pole axis, where the gain is largest, is where the isotropy is worst. The upper poles reach a slightly lower minimum than the lower poles, consistent with the half-cut asymmetry seen on the previous slide. All three planes look essentially the same, showing that the isotropy inherits the overall symmetry of the six-pole layout.
Isotropy
P1
P3
P2
P4
P2
P5
P6
P1
Isotropy
P4
P5
P6
P3

## Slide 26: Quantitative Assessment of Multi-Pole Actuators
DesignA
Using the same calibrated model, the three singular values σ₁ ≥ σ₂ ≥ σ₃ at every real FEM node in the workspace are histogrammed separately All three share one set of bins and are each normalised to a percentage, so the bar heights are directly comparable.Both histograms have the same resolution (0.02mT/A).
Within the calibration radius Design A behaves as an essentially direction-independent three-degree-of-freedom actuator: the three principal gains differ by only 13.5 %, no direction is weak enough to be unusable, and the controller needs no extra margin for any particular axis. What sets the usable authority is the weakest axis σ₃, whose mean is 13.85 mT/A with only 1.5 % variation — the worst-case actuation capability is therefore very nearly a constant across the whole workspace and can be taken directly as a design value. Almost all of the spread comes from the strongest axis σ₁ (3.7 % variation), but since performance is governed by the weakest axis this fluctuation does not affect the guaranteed capability. The three peaks are clearly separated yet all fall within the narrow band of 13.4–17.3 mT/A, overlapping only on their adjacent flanks — direct evidence that the hexapole remains well-conditioned at this radius.
Mean | 15.722 | 14.403 | 13.852
 | 15.722 | 14.403 | 13.852
Capacity measure
Percentage count

## Slide 27: Quantitative Assessment of Multi-Pole Actuators
DesignA
Mean | 14.6246
 | 14.6246
Mean | 0.8836
 | 0.8836
Capacity measure
Percentage count
Histogram resolution:0.02 mT/A
Histogram resolution:0.02
Isotropy
Percentage count

## Slide 28: Quantitative Assessment of Multi-Pole Actuators
DesignA
Mean | 14.6246
 | 14.6246
Mean | 0.8836
 | 0.8836
Histogram resolution:0.02 mT/A
Histogram resolution:0.02
Capacity measure
Percentage count
Isotropy
Percentage count

## Slide 29: Quantitative Assessment of Multi-Pole Actuators
DesignB
The capacity measure 𝒞 for Design B is mapped on the same three actuator planes, with a colour scale of 30–55 mT/A. The model is calibrated on the converged design within R ≤ 150 µm and evaluated point by point out to the pole-tip sphere at R = 500 µm, with the in-plane pole pairs marked on the rim.
The spatial pattern matches Design A: the centre sits mid-range at about 38 mT/A, 𝒞 rises monotonically along a pole axis to a maximum of about 51 on the rim, and falls to about 31 on the rim between poles, a directional variation of roughly 1.6× at the outer edge. The overall level is about 2.6× that of Design A (37.96 vs 14.39 mT/A at the centre), and this ratio holds across radii and directions, so the gain is raised as a whole rather than the field shape being altered. One difference from Design A is that the six lobes are nearly equal in strength (50.6–51.1 mT/A, about 1 % spread), with no splitting into upper and lower groups — a consequence of the planar hexapole's up–down symmetry.
P3
P2
P4
P5
P6
P1
P2
P1
Capacity measure
P4
P5
P6
P3
Capacity measure

## Slide 30: Quantitative Assessment of Multi-Pole Actuators
DesignB
Isotropy for Design B is mapped on the same three actuator planes, with a colour scale of 0–0.8. The model is calibrated on the converged design within R ≤ 150 µm and evaluated point by point out to the pole-tip sphere at R = 500 µm, with the in-plane pole pairs marked on the rim.
Design B is markedly less isotropic than Design A across the whole workspace: κ at the centre is only 0.54 against 0.95 for Design A. The shape of the distribution also differs — the high- region is not a concentric core about the origin but two off-centre lobes along a diagonal, with the best values of 0.60–0.65 occurring roughly 130–175 µm from the centre, only slightly above the 0.54 found at the centre itself. The decay with radius is faster as well, reaching 0.06–0.24 at the rim, with the lowest values along the pole directions. Taken together with the previous slide, the planar hexapole trades isotropy for roughly 2.6× the gain: actuation is stronger overall, but the three principal axes are less balanced and there is no simple "stay at the centre" strategy for best conditioning.
P3
P2
P4
P5
P6
P1
P2
P1
Isotropy
P4
P5
P6
P3
Isotropy

## Slide 31: Quantitative Assessment of Multi-Pole Actuators
DesignB
Mean | 50.196 | 45.304 | 27.105
 | 50.196 | 45.304 | 27.105
Using the same calibrated model for Design B, the three singular values σ₁ ≥ σ₂ ≥ σ₃ at every real FEM node in the workspace are histogrammed separately (in mT/A), sharing one set of bins (0.1mT/A wide) and each normalised to a percentage. Note that this bin width differs from the Design A histogram, so bar heights are comparable among the three series here but not across the two slides.
The three distributions fall into two clear groups: σ₁ and σ₂ sit close together while σ₃ averages just 27.1 mT/A and is separated from the other two by a gap containing no samples at all. The controllable set is therefore an oblate ellipsoid — two comparable strong axes and one distinctly weaker axis — rather than a near-sphere, matching the imbalance of σ₁/σ₃ ≈ 1.85. The usable authority is set by the weakest axis: σ₃ ≈ 27.1 mT/A is still about twice the weakest axis of Design A (13.9 mT/A), so despite the poorer directional balance Design B remains stronger in its worst direction. The cost is slightly less positional stability, σ₃ varying by 5.6 % across the workspace against 1.5 % for Design A.
Capacity measure
Percentage count

## Slide 32: Quantitative Assessment of Multi-Pole Actuators
DesignB
Mean | 39.4683
 | 39.4683
Mean | 0.5415
 | 0.5415
Histogram resolution:0.1 mT/A
Histogram resolution:0.02
Capacity measure
Percentage count
Isotropy
Percentage count

## Slide 33: Quantitative Assessment of Multi-Pole Actuators
DesignB(Have gap)
Design B with a 100 µm gap(The air gap is located at the junction between the six guide posts and the magnetic poles.): the capacity measure 𝒞 on the same three actuator planes, colour scale 18–33 mT/A. The model is calibrated on the converged design within R ≤ 150 µm and evaluated point by point out to the pole-tip sphere at R = 500 µm.
The spatial pattern is identical to the no-gap case: the centre sits mid-range at 23.1 mT/A, 𝒞 rises along each pole axis to 30.3–30.8 at the rim, and falls to about 19.5–20.7 on the rim between poles, with the six lobes still nearly equal. Only the overall level changes — the centre drops from 37.96 to 23.08 mT/A and the rim maximum from about 51 to about 31, roughly 0.61× the no-gap design throughout. The gap therefore reduces the gain itself while leaving the field shape and its directional character unchanged.
P4
P5
P6
P3
Capacity measure
P3
P2
P4
P5
P6
P1
P2
P1
Capacity measure

## Slide 34: Quantitative Assessment of Multi-Pole Actuators
The same gap calibration, now mapping isotropy κ = σ₃/σ₁ on a colour scale of 0–0.8, over the same evaluation range as the previous slide.
The isotropy pattern also matches the no-gap case: the high- region is again offset from the origin and split into two diagonal lobes, with best values of 0.56–0.61 at roughly 160–215 µm from the centre, while the centre itself is 0.46; the rim falls to 0.06–0.27, lowest along the pole directions. Compared with the no-gap design, is slightly lower everywhere and the bright lobes sit a little further out. The gap's main cost therefore remains the gain, which drops to 0.61×, while isotropy degrades only modestly and the characteristic that the best-conditioned point is not the origin is unchanged.
DesignB(Have gap)
P4
P5
P6
P3
Isotropy
P2
P4
P5
P6
P1
P2
P1
P3
Isotropy

## Slide 35: Quantitative Assessment of Multi-Pole Actuators
Mean | 32.34 | 27.588 | 15.54
 | 32.34 | 27.588 | 15.54
Design B with the gap: the three singular values σ₁ ≥ σ₂ ≥ σ₃ at every real FEM node in the workspace, histogrammed separately on one shared set of bins 0.05mT/A wide, each normalised to a percentage. This bin width differs from the other slides, so bar heights are comparable only among the three series here.
The structure matches the no-gap case and still falls into two groups: σ₁ and σ₂ average 32.3 and 27.6 mT/A while σ₃ is only 15.5 mT/A, separated from the other two by a gap containing no samples, so the controllable set remains an oblate ellipsoid. The imbalance is somewhat worse, however — σ₁/σ₃ rises from 1.85 without the gap to 2.08, the σ₁–σ₂ separation widens from 10.8 % to 17.2 %, and their overlap nearly vanishes. The weakest axis σ₃ drops to 0.57× its no-gap value but still exceeds Design A's 13.9 mT/A, so even with the gap the planar hexapole retains more authority in its worst direction than the conical one.
DesignB(Have gap)
Capacity measure
Percentage count

## Slide 36: Quantitative Assessment of Multi-Pole Actuators
Mean | 23.9991
 | 23.9991
Mean | 0.4820
 | 0.4820
DesignB(Have gap)
Histogram resolution:0.05mT/A
Histogram resolution:0.02
Capacity measure
Percentage count
Isotropy
Percentage count

## Slide 37: Quantitative Assessment of Multi-Pole Actuators
Mean | 24 | 39.468
 | 24 | 39.468
The capacity measure and the isotropy κ of the gap and no-gap versions are overlaid for direct comparison. Each series is normalised to a percentage and both share one set of bins (0.05 mT/A for , 0.01 for ), so bar heights within each panel are directly comparable.
The two metrics respond very differently to the gap, and the reason is their differing sensitivity to overall scale. is proportional to the overall gain: the gap inserts extra reluctance in each pole's magnetic circuit, so less flux reaches the tip for the same current and falls directly to 0.658×. The two distributions are consequently fully separated, the mean dropping from 39.47 to 24.00 mT/A (0.61×) while the width is essentially unchanged (about 1.7 % variation in both) — a bulk shift rather than a change of shape., being the ratio σ₃/σ₁, is insensitive to overall scale and reflects only the relative distribution among the six poles; since the gap widens the pole-strength spread from 13.3 % to 27.5 %, falls only slightly, from 0.542 to 0.482 (0.89×), and the two distributions overlap substantially. The cost of the gap therefore falls almost entirely on strength,
DesignB(Have gap & No gap )
Mean | 0.4820 | 0.5415
 | 0.4820 | 0.5415
Capacity measure
Percentage count
Isotropy
Percentage count

## Slide 38: Reference
, where

## Slide 39: Reference
Two layouts of the same planar hexapole, both with the workspace radius defined as . In Design B the six poles sit inside a square yoke frame; Design C keeps the identical pole-tip geometry and pole-tip sphere radius but re-routes the return path into six separate arms in a star arrangement, each with a coil bore at its outer end. The two differ in pole length and outer return structure, not at the tips.
P1
P2
P3
P6
P4
P5
DesignB
DesignC
P1
P5
P3
P2
P6
P4

## Slide 40: Reference
Design C is calibrated on the converged design within R ≤ 150 µm, listing , , and NMAE for the single-parameter (13 points) and eighteen-parameter (7 points) fits.
The layout change the diagonal of tightens from 0.7359–0.8333 in Design B (a spread of 13.25 %) to 0.8175–0.8333 (1.93 %), so the six poles are now almost equal in self-excitation, showing that re-routing the return path removes the pole-strength inequality of the earlier layout. barely moves (744 → 768 µm) and the fit quality is comparable to Design B, with NMAE of 9.84 % for single and 0.76 % for eighteen parameters.
(7 points)

## Slide 41: Reference
The isotropy of Designs B and C is overlaid on a single histogram, both series sharing one set of bins 0.01 wide and each normalised to a percentage.
Even though the diagonal of is now almost perfectly uniform in Design C, the isotropy does not improve: the mean falls slightly from 0.542 to 0.502, the whole distribution shifting left, with the two overlapping substantially. Comparing all three designs makes the point clearer — Design A has the largest diagonal spread (16.5 %) yet by far the highest(0.95), while Design C has the most uniform diagonal (1.9 %) and the lowest . Isotropy is therefore not determined by whether the six poles are equally strong, nor by the pole length; it is set by the geometric arrangement of the poles themselves, that is, the directions and mutual angles at which they are placed. Changing the layout brought the pole strengths into line but left that angular arrangement untouched, which is why the isotropy did not follow; improving it requires acting on the pole-axis directions.
Calibration results
 | esignB | DesignC
Mean | 0.5415 | 0.5023
 |  | DesignC
 | 0.5415 | 0.5023
Isotropy
Percentage count

## Slide 42: Reference
(1771 points)

## Slide 43: Reference
(1791 points)

## Slide 44: Reference
(13 points)

## Slide 45: Reference